## Slide 1: pyNTM Training Module 3 – modifying the Model and what if simulations
Network Traffic Modeler in Python3

## Slide 2: Course Topics
Adding a new Node
Adding a new link
Adding traffic to the traffic matrix
Changing Interface/Circuit capacity
Changing an Interface metric
Working with RSVP LSPs

## Slide 3: Exercise setup

## Slide 4: Copy the repository zip file to a practice directory and unzip it
Copying the repository will allow you to use some of the additional tools to improve your user experience
  Visualization
  Simple user interface

## Slide 5: Set up your virtual environment (optional)
Go into the archive directory
  Look for requirements.txt
Follow directions below to create the virtual environment
Example is to the right 
A virtual environment provides an isolated environment and ensures no interference from existing installations and/or dependencies

## Slide 6: Let’s get started!
Switch to the examples directory in the repository
Start python3
Append parent directory to your sys path
  Allows imports from folders in the parent
Import the Model object
Load Model from data file
  sample_network_model_file.csv has Interfaces, Nodes, and Demands
  IGP only
  no RSVP LSPs in the file
Observe node objects

## Slide 7: Visualization (beta) - optional
Requires full repository download from github or extract the module
  Easy access via the virtual environment setup from earlier in this guide
  Reference the Exercise setup earlier in this presentation for full instructions to set up the environment to use the repository
Make sure the model is converged!
  model1.update_simulation()  model1 is the Model object
graph_network_interactive.make_interactive_network_graph call
  Takes Model object as argument
  uses mpld3 python package under the covers
Produces interactive graph in browser with tool tips, an interactive legend, and draggable Nodes and Interface endpoints for easier viewing
Uses a Node’s lat/lon (y,x) attributes to position Node on layout
The Interface from B to A is 0-24% utilized
The Interface from A to B is over 100%
Interactive legend
All nodes and circuit midpoints are movable
Tooltips appear when hovering over interfaces and nodes

## Slide 8: Add a new Node
Import the Node object
Define Node(‘Z’)
Assign latitude/longitude (y, x) coordinates
Add Node(‘Z’) to the Model
Examine the Model
  Now there are 9 Nodes
An orphan Node has no interfaces

## Slide 9: Add a new Circuit between Node(‘A’) and Node(‘Z’)
Use the Model add_circuit call
  New circuit will have a metric of 10 on both sides and a capacity of 200
Update the simulation
Visualize topology with new Node(‘Z’) (optional)

## Slide 10: Adding a Demand to the traffic matrix
Use the Model add_demand method
Find new demand’s path

## Slide 11: Changing Circuit Capacity
Change the capacity of the Circuit between Node(‘A’) and Node(‘B’) from 100 to 200
Change capacity attribute of each Interface in the Circuit
  circuits_with_mismatched_interface_capacity
  Capacities must match or Model will throw a ModelException
Be sure to update the simulation after the change!
  model1.update_simulation()

## Slide 12: Changing Interface cost (metric): Use Case
From our prior visualization, we see the Interface on Node(‘F’) facing Node(‘E’) is over 100% utilized
There are two demands on that Interface; below we see the path(s) for each demand
  Notice that the demand from Node(‘F’) to Node(‘B’) splits over 2 ECMP paths

## Slide 13: Changing Interface cost (metric)
Let’s see how changing the metric on the Interface on Node(‘F’) facing Node(‘E’)
Simply modify the cost attribute on the Interface and update the simulation
Examine the utilization

## Slide 14: FIN